## Slide 1: Optimizing Radical Evolution: TOPAS Simulations for High-Intensity Polarized Targets
TOPAS Monte Carlo Simulation - Geant4
Samuel Takwirira, Karl Slifer, PhD – UNH Nuclear Physis Group

## Slide 2: The Physics of Radiolytic Depletion
Target Material: Frozen ammonia ( or Deuterated Ammonia
The Radical Paradox:
  Creation: High-energy electron beams create paramagnetic centers (radicals) necessary for Dynamic Nuclear Polarization (DNP).
  Depletion: Excessive local energy deposition (over-irradiation) causes "radiolysis," where existing radicals are destroyed or recombined into non-paramagnetic species.
The Ultimate Goal: Maintain the optimal radical concentration () typically in the range of to .
Immediate Goal: Achieve Uniform Dose distribution across the target volume

## Slide 3: Why Uniform Dose is Critical
Polarization Gradient: DNP enhancement is a function of radical density If the beam creates a "hot spot," that region over-depletes, dropping the local polarization .
Thermal Management: Non-uniform dosing leads to local heating, which exponentially increases the nuclear spin-lattice relaxation rate (), effectively "killing" the polarization.
Even a few of local heating can significantly shorten the nuclear relaxation time (), causing a massive drop in steady-state polarization.

## Slide 4: Experimental Set Up
First Use of a Longitudinally Polarized Target with CLAS12 C.D. Keith, J. Brock, C. Carlin, T. Kageya V. Lagerquist, J. Maxwell, and P. Pandey

## Slide 5: Methods & Tools
TOPAS Monte Carlo – TOol for PArticle Simulation.
  Originated in the Medical Physics community – Used for Treatment Planning Systems (TPS) in Radiation Oncology Research
  “g4em-standard_opt4” Physics Module
  “DoseToMedium” Scorer
  i:So/ElectronSource/NumberOfHistoriesInRun = ( days to run!!!)

## Slide 6: Irradiation Method Rotation by
Define a cylinder on the interval z ∈ [0, L] with radius R.
Dose from a source located at z = 0 is = f (r, θ, z)
Irradiation from z = L reflection across the mid-plane
The second dose is defined as (r, θ, z) = (r, θ, L − z)
The total dose is (r, θ, z) = (r, θ, z) + (r, θ, L − z)
z=L
z=0
R
Mirror Plane

## Slide 7: Modeling the Lab Set Up

## Slide 8: The TOPAS Outputs
CSV files (.csv) Format for most Scorers (Dose, Fluence, e.t.c)
Binary files (.bin) High-speed, large-scale data storage for Phase Space
ROOT files (.root) Native format for the CERN ROOT framework
DICOM files (.dcm) Exporting dose distributions into clinical systems
Graphic/Visual Outputs
  Includes OpenGL (GUI), VRML (.wrl), Digital Asset Exchange files (.dae), PDF/PostScript, XML for specialized geometry exports/parameter logging

## Slide 9: What is in the CSV File?
Shows Absorbed Dose vs. Depth into the material (z-axis):
,
Where:
* = Absorbed Dose [Gy= Jkg-1]
  * = Individual energy deposit from the particle interaction [J]
  * = Density of the target material
  * = Volume of the scoring voxel [m3]

## Slide 10: The Chemical Yield (the G-Value)
To relate energy to chemical change, we use the G-value, defined as the number of radicals produced per 100 eV of absorbed energy:
    G =

## Slide 11: The Unit Conversion Constant (k)
Because is in Joules/kilogram and is desired in , we define a conversion constant (or its inverse ) to align the units:
= 6.242 ×

## Slide 12: Final Radical Density ()
Combining the TOPAS dose, the material density, and the G-value, the final radical density is calculated
as:
In practical units, is in g/cm3 and is in Gray)
≈ (6.242 × 1013) · G · D · in

## Slide 13: Definitions and Acronyms
DICOM: Digital Imaging and Communications in Medicine
DNP: Dynamic Nuclear Polarization
TOPAS: Tool for Particle Simulation (Monte Carlo – Geant 4)

## Slide 14: Sources Cited
Framework: Perl J, et al. TOPAS: An innovative proton therapy simulation framework. Med Phys. 2012;39(11):6818-35.
Radical Physics: Crabb DG, Meyer W. Solid Polarized Targets for Nuclear and Particle Physics. Annu. Rev. Nucl. Part. Sci. 1997. 47:67-109.
Radiolysis Modeling: Ramos-Méndez J, et al. TOPAS-nBio: An extension to the TOPAS simulation toolkit for cellular and sub-cellular radiobiology. Phys Med Biol. 2019.
Target Kinetics: London GW, et al. Radiation damage in polarized target materials. NIM A. 1994.

## Slide 15: 806 Research Requirements
Poster presentation (3/13—2:10-3PM) based on what you know and remember from what you have learned.
Maker Space to print the poster by Friday morning at the latest –somewhere in Kingsbury – Mention it is for a class so that I don’t have to pay.
GRC Presentations – register by 3/16 – 4/13 (Oral) and 4/15 (Poster)
End of April/Early May – Last Day of Class
Proposal – Written: Due at the end of finals (Pages Max)